## Slide 1: Building Electronics for High Energy Nuclear and Particle Physics Experiments
Discuss several systems I have built in the past
  PHENIX experiment Hadron Blind detector digitizer readout system
  Data Collection Module upgrade for the PHENIX experiment
  MicroBooNE Neutrino Liquid Argon TPC Front End Board
Some discussion on
  Future sPHENIX experiment calorimeter electronics
Lessons learnt in building electronics projects.

## Slide 2
PHENIX experiment in RHIC at BrookHaven National Lab.
Heavy Ion Physics
p + p Spin Physics
HBD
2006-2009

## Slide 3
Front-End
Module (FEM)
Data Collection
Module(DCM)
Sub-Event
Buffer
JSEB
Assembly Trigger processor (ATP)
Front-End
Module (FEM)
Data Collection
Module II(DCM II)
Sub-Event
Buffer
JSEB II
Assembly Trigger processor (ATP)
Ethernet Switch
Archive
PHENIX Online System
RHIC clock is about 9.8 MHz
depend on collision specs.
Level 1 trigger delay is 40 beam crossing
L1 trigger rate is 10 KHz.
To keep system live time near ~100%,
FEMs store 5 L1 triggered events
Frontend are built by various groups.
DCM & DCM II are used to interface
with all the FEMs.
(first stage of the event builder)
L1 trigger
on
detector
off
detector
(upgrade)
(baseline)

## Slide 4
Honeycomb panels
Mylar entrance window
HV panel
Pad readout plane
HV panel
Triple GEM module with mesh grid
Mesh
CsI layer
Triple
GEM
Readout Pads
e-
Primary ionization
g
HV
Proximity focus Cherenkov counter. (sensitive only to electron)
Use CsI to convert photon to electron.
GEM is used for amplify the electron from CsI.
Measure time and charge
2006 - 2009
HADRON BLIND
DETECTOR

## Slide 5: Charge Preamp with On-Board Cable Driver (IO1195-1-REVA)
Features:
+/- 5V power supply.
165 mW power dissipation.
Bipolar operation (Q_input = +/- )
Differential outputs for driving 100 ohm twisted pair cable.
Large output voltage swing -- +/- 1.5V (cable terminated at both ends)
        (+/- 3V at driver output)
Low noise: Q_noise = 345e (C_external = 5pF, shaping = .25us)
        (Cf = 1pF, Rf = 1meg)
Size = 15mm x 19mm
Preamp output (internal) will operate +/- 2.5V to handle large pile-up.
Preamp (BNL IO-1195)
2304 channels total
19 mm
15 mm

## Slide 6
S-
S+
G
S-
S+
Signal arrangement
Use 2MM Hard Metric cable to move signals between preamp/FEM
2mm HM connector has 5 pins per row and 2mm spacing between pins and rows
There are two types of cable configuration:
*100 ohms parallel shielded cable
50 ohms coaxial cable
Our choice is
This gives us signal density 2mm x 10mm for every 2 signals.
Same type of cables will be used for L1 trigger data.
MERITEC

## Slide 7
FEM receiver + ADC
8 CHANNEL 65 MHz 12 bits ADC (80 TQFP)
The +/- input can swing from 1V to 2V, Vcm=1.5V
+ side 2V, - side 1V -> highest count
- side 2V, + side 1V -> lowest count
Our +/- input will swing from 1.5 to 2V/ 1.5 to 1V
we will only get 11 bits out of 12 bits
16fc will be roughly sitting at 200 count
We will run the ADC at 6X beam crossing clock
6X9.4 MHz = 56.4 MHz or ~17.7ns per samples
ADC data are serialized LVDS at 12*56.4 MHz= 678 MHz
Differential
Receiver
ADC
Preamp
Cable driver
FPGA
Based on AD8138 receiver
Unity gain
TI ADS5272

## Slide 8
Signals from Preamp
HBD ADC board
Differential
receiver
ADC
ALTERA
FPGA
48 channels per board
6U X160 mm size
We use ALTERA STRATIX II 60 FPGA to receive the 6 ADC’s data (8 channel per ADC)
It has 8 SERDES blocks. ALTERA provides de-serializer Mega function block.
6XADC clock  SERDES clock
 data de-serialized as 6 bit 120 MHZ
 Regroup to 12 bits at 60 MHz , 45 degree phase adjustment step. Timing Margin  270 degree.
The FPGA also provides
L1 delay (up to 240 samples)
8 events buffer
ADC setting download
Offline slow readback
7 threshold levels for L1
trigger primitives per channel.

## Slide 9
Pedestal Run
Width s (ch)
Width s (ch)
Mean (ch)
Mean (ch)
Channel #
Channel #
Electronics Rack

## Slide 10: Data Collection Module II (DCM II)
Receives all the data from the upgrade detectors frontend modules
Provide 5 event buffers for the FEMs.
  Data transmission time is based on average trigger rate.
  to achieve minimum trigger deadtime.
FEM’s data are not compressed. DCM II compresses the raw data and formats the data for the Event builder.
Collects the compressed FEM data to the event builder
Error monitoring.
Provides slow readback path for detector readout without the event builder.

## Slide 11
TLK
2501
65kx18
FIFO
compressor
32KX32
Dual port
256X45
Header
FIFO
M
U
X
busy
16Kx32
FIFO
Demux
Align
64KX32
Dual port
256X60
Header
FIFO
TLK
2501
65kx18
FIFO
compressor
32KX32
Dual port
256X45
Header FIFO
busy
(FIFO has more
than 16K words)
1.6 Gbits/sec
Optical link
1.6 Gbits/sec
Optical link
detector
dependent
Event number
Memory address
Word counts
M
U
X
Test
data
9bits X 4
at 480 MHz
80 M words
( 16bits wide)
Link
port
Data
In/out
Token
In/out
16Kx32
FIFO
Demux
Align
16Kx32
FIFO
Demux
Align
16Kx32
FIFO
Demux
Align
9bits X 4
at 480 MHz
slow control
/download
48 V
on/off
FPGA
Download
control/
readback
TLK
2501
65kx18
FIFO
compressor
32KX32
Dual port
256X45
Header
FIFO
M
U
X
busy
TLK
2501
65kx18
FIFO
compressor
32KX32
Dual port
256X45
Header FIFO
busy
(FIFO has more
than 16K words)
1.6 Gbits/sec
Optical link
1.6 Gbits/sec
Optical link
detector
dependent
Event number
Memory address
Word counts
Test
data
80 M words
( 16bits wide)
9bits X 4
at 480 MHz
Test
data
Test
data
Test
data
DATA COLLECTION MODULE II
(DCM II)
Interface to the frontend electronics
Compress/Merge/5 events bufferError checking data packet
Used in VTX (strip and Pixel), FVTX
8 1.6 Gbits/sec optical ports per module
Individual ports can be enabled or disabled
8 80 MHz 16bits words in  80 MHz 32 bits word out
Stratix III
hold
hold
(LVDS)

## Slide 12
DCM II
token,hold
data, busy
Token/demux/align/busy/hold
Buffer
optical
transceiver
buffer
buffer
PCI express
IP core
optical
transceiver
optical
transceiver
optical
transceiver
DCM II
DCM II
Timing
System
data, busy
token,hold
L1 System
busy
Mux/demux
Buffer
optical
transceiver
buffer
buffer
PCI express
IP core
optical
transceiver
optical
transceiver
controller
JSEB II
JSEB II
Partitioner III
DCM II DATA
FLOW DIAGRAM
Partition module output data with 2 3.125 Gbits optical link to JSEB module. The hold is returned via optical link.
Controller allows us to:
Download FPGA code and setup system parameters.
Readback system status and provide a data readback path during detector commissioning.
40 MHz 8 bits data
+ 2 bits control

## Slide 13
DCM modules
DCM crate
In
PHENIX
DCM II system first production was done for
vertex strip and pixel detector &
forward vertex in 2010
JSEB II Module

## Slide 14: Cryostat: Keeps Ar liquid < 87.3oK
Drift
Welded
Cryostat
MicroBoone Experiment
Liquid Argon TPC detector
For Neutrino Physics
p0  gg
simulation
Electronics Platform
Cryostat

## Slide 15: Overall Electronics scheme
Blue  Nevis
8256 Time Projection Chamber wires
32 PMT’s provide a neutrino trigger
in time with beam gate

## Slide 16: FEM Concept
Build a system that can take both triggered data (lossless compression) and continuous recording (lossy compression).
  System is running continuously.
  Record both Neutrino events / SuperNova events.
The FEM (frontend module) organizes ADC data as frames.
  Grouping/processing of the frame depends on whether there is trigger or not.
  The neutrino event will consist of several frames.
  If no trigger, the frames will be continuously recorded.
Once the data is processed, the events will flow to the computer in separate paths.
  Keep neutrino and SuperNova events’ flows as independent as possible
   easier to prioritize the event flow.

## Slide 17
frame
frame
frame
frame
trigger
write
pointer
read
pointer
16 MHz
clock
Frame
synch
FPGA
PLL
16MHZ
ADC clock
128 MHz Frame
buffer clock
ADC
ADC
ADC
ADC
decimation
decimation
decimation
decimation
128MHz
1M X 36
SRAM
Frame
Data
trigger
r/w
address
16 MHz ADC
 2 MHz sample
The system clock is free running.
It is not synch with the accelerator.
Data Sample memory
Time
supernova
Neutrino
Arrange the sample memory into 4 frames
Each frame can store up 2ms of data
(currently set at 1.6ms)
Sampling speed set a 2MHz maximum
 2MHz* 64 channel =128MHz 16 bits word
 64 MHz 32 bits word (2 ADC’s / word)
(sampling frequency drive memory speed)
Use alternate cycle for write/read (100% live)
Init(/Run)
M
U
X
Downsampling +
anti-aliasing filter

## Slide 18
ADC
demux
/align
/decimation
Frame generator
SRAM write/read
SRAM
fake
data
trigger
Neutrino
compressor
header
Pre-buffer
16KX40 FIFO
Hamming code/packing
DRAM
Pointer FIFO
LINK
SuperNovacompressor
header
Pre-buffer
16KX40 FIFO
Hamming code/packing
DRAM
Pointer FIFO
LINK
Neutrino Path
SuperNova Path
Neutrino
Token
Neutrino
Data
SuperNova
Token
SuperNoa
Data
3 16 bits word 
2 24 bits word 
2 30 bits ECC words
(5+1 parity)
Huffman code by
(Jin-Yuan Wu)
Difference 0 assign code 0
+1 assign code 1
-1 assign code 2 etc
Need compression factor 20 to 80
Probably will use some threshold plus
Huffman coding
(remove as much noise as possible)
Slow
Control
readback
Slow
Control
readback
Link data
Neutrino token
Has priority over
Supernova token
Read has priority over
Write on DRAM access
Event number
Word count
memory address
2 sample per cycles
Read/write every
other cycle
TPC DATA PROCESSING
DATA FLOW

## Slide 19
PMT
shaper
ADC
Post-pre
diff(i) =
Ph(i+n)- ph(i)
compare
diff(i) >
Threshold(ch)
1KX33 FIFO
Pack 2 samples
into one word
wr
packetize
Trigger Logic
Neutrino
gates
PMT
shaper
ADC
Post-pre
diff(i) =
Ph(i+n)- ph(i)
compare
diff(i) >
Threshold(ch)
1KX33 FIFO
Neutrino
gates
packetize
PH(max) & width
S
R
A
M
Trigger
Module
NHITS,
PHSUM
Beam
Cosmic
Michel
40 channels
Frame number
sample number
64 MHz
clock
64 MHz
clock
PMT DATA PROCESSING
PMT DATA PROCESSING
DATA FLOW
PMT data is sampled at 64 MHz. It is not possible to write all this data into SRAM with the available frame space
Only keep the data associated with discriminator firings (neutrino data + cosmic rays).
(* data compression before buffer*)

## Slide 20
We went through two production cycle:
1) For Microboone ( early last year)
147 FEM modules
5 PMT ADC modules
and supporting modules for 10 crates
2) For LANL (late last year)
54 FEM modules
and supporting modules for 5 crates
FEM Board
Stratix III
DRAM
SRAM
TPC ADC
+ FEM board
PMT ADC
+ FEM board

## Slide 21: The sPHENIX Detector
Solenoid
Solenoid
Magnet
HCAL
EMCAL
VTX

## Slide 22: Original Concept: Optical Accordion (EM section)
Accordion design similar to ATLAS Liquid Argon Calorimeter
Want to be projective
in both r-f and h
Accordion prevents channeling
and allows readout on the front
or back of the absorber stack
Can make projective in r-f by
tapering thickness of tungsten
plates
Can make projective in h by
fanning out fibers
Oscillations must be kept small
because of minimum bending
radius of fibers and plates
Readout
Towers
Plates
Fibers
Particle

## Slide 23: HCAL Readout
Scintillating tiles with WLS fibers embedded in grooves
Fibers read out with SiPMs
T
2x11 segments in h (Dh =0.1)
64 segments in f (Df =0.1)
1408 x 2(inner,outer) = 2816 towers
2x11 scintillator tile shapes
Inner
Outer
Inner readout
(~10x10 cm2)
Outer readout
SiPMs + mixers
8 readout fibers per tower

## Slide 24: Discrete Preamp
Cd = 640pF for dual SiPM, Ist stage Av = 65, multi-pole differential output filter

## Slide 25: sPHENIX Calorimeter digitizer electronics
Similar to HBD ADC system.
  We will use 14 bits ADC instead of 12 bits ADC while maintaining speed at 60 MHz
    Including offset to deal with signal only swing one side
  Better cables and connector arrangement.
    Instead of ~ 2400 channel  30,000 channel
    48 channels/board  64 channel board
  Add optical output for L1 trigger primitives output.
  Add secondary path for short trigger summary output.
  Instead of using LVDS to multiplex data between modules, we will use multiple Gbits transceivers to pass the data between the modules.
Mini SAS

## Slide 26: Cost & Schedule
Understand the major cost of the system.
  Most of the majors components, ADC, FPGA etc. Past printed circuit board and assembly cost.
Estimate the cost of the system within some margins.
  You have to cover some unknown cost that could happen down the road.
  Boss always pushes initial cost lower and will be much more unhappy if you have to ask more fund at the tail end of the project:
    This is the time when the project has less money and less freedom of where to spend it.
Estimate the schedule conservatively
  Prototype has lots of unknown both technically or surprise from detector group.
  Testing always takes longer
  Production has to deal with real world schedule, like part shortage….
  Surprise in the production..

## Slide 27: Design Specification
Carefully discuss the specification of the readout electronics
  In the proposal stage, detector specification almost always idealized.
    Always try to build more than they ask.
    Occupancy of the detectors are under-estimated.
    Don’t be surprised, if they come back ask for more after the initial design is done.
  Try to have a conservative design.
Don’t under estimate number of prototype modules needed
  Before production, prototypes are needed for detector group, DAQ group, your lab.
  Don’t give out the prototype system freely.
    It needs lot of support.
  PCB manufacture produce boards with a minimum lot. The cost of one board and 10 boards may be exactly the same.
    For a small system, the extra boards could be used for the productions if it is successful.

## Slide 28: Prototype
We have done the last 4 readout systems where the prototype is the production design with only pre-cautionary modification except for 1 module. This is achieved by
  Don’t fabricate anything till all the boards are designed.
  Finish the FPGA design enough till all the I/O pins are done.
  Work out the testing method and all testing features that are needed.
  Our engineers design/layout the board. I independently check the board.
    I normally read all the data sheets carefully. Check the layout compared to the data sheets.
    Check the FPGA pin out against the layout. Read the small footprints.
    Check the mechanical dimensions. Mounting holes placement.
    Get parts. Put parts on the layout printout to check footprint.
    Figure out the power up state of the board.
      Check the pull up and pull down of lines critical during the startup.
    Talk to board assembler about the component placement restrictions near the connectors.
    When the design is revised, re-check everything again.
    Look at the checkplot.

## Slide 29: The past decade
Because we only work on small projects without extended reviews. It allows us to use up-to-date technologies.
  We spend most of time just on building electronics and make sure it will run smoothly in the experiments.
  It is a continuous design/prototype/fabrication cycle during the past decade.
Helped by the our engineers, we have built 4 readout systems for PHENIX and MicroBooNE experiements.
  MicroBoone will fill the tank with liquid Argon sometime around the summer.
We will proceed to prototype the sPHENIX EM & Hadron calorimeters digitize system in the next 1.5 years.

## Slide 30
13 Countries; 71 Institutions
Abilene Christian University, Abilene, TX 79699, U.S.
Baruch College, CUNY, New York City, NY 10010-5518, U.S.
Collider-Accelerator Department, Brookhaven National Laboratory, Upton, NY 11973-5000, U.S.
Physics Department, Brookhaven National Laboratory, Upton, NY 11973-5000, U.S.
University of California - Riverside, Riverside, CA 92521, U.S.
University of Colorado, Boulder, CO 80309, U.S.
Columbia University, New York, NY 10027 and Nevis Laboratories, Irvington, NY 10533, U.S.
Florida Institute of Technology, Melbourne, FL 32901, U.S.
Florida State University, Tallahassee, FL 32306, U.S.
Georgia State University, Atlanta, GA 30303, U.S.
University of Illinois at Urbana-Champaign, Urbana, IL 61801, U.S.
Iowa State University, Ames, IA 50011, U.S.
Lawrence Livermore National Laboratory, Livermore, CA 94550, U.S.
Los Alamos National Laboratory, Los Alamos, NM 87545, U.S.
University of Maryland, College Park, MD 20742, U.S.
Department of Physics, University of Massachusetts, Amherst, MA 01003-9337, U.S.
Morgan State University, Baltimore, MD 21251, U.S.
Muhlenberg College, Allentown, PA 18104-5586, U.S.
University of New Mexico, Albuquerque, NM 87131, U.S.
New Mexico State University, Las Cruces, NM 88003, U.S.
Oak Ridge National Laboratory, Oak Ridge, TN 37831, U.S.
Department of Physics and Astronomy, Ohio University, Athens, OH 45701, U.S.
RIKEN BNL Research Center, Brookhaven National Laboratory, Upton, NY 11973-5000, U.S.
Chemistry Department, Stony Brook University,SUNY, Stony Brook, NY 11794-3400, U.S.
Department of Physics and Astronomy, Stony Brook University, SUNY, Stony Brook, NY 11794, U.S.
University of Tennessee, Knoxville, TN 37996, U.S.
Vanderbilt University, Nashville, TN 37235, U.S.
Universidade de São Paulo, Instituto de Física, Caixa Postal 66318, São Paulo CEP05315-970, Brazil
China Institute of Atomic Energy (CIAE), Beijing, People's Republic of China
Peking University, Beijing, People's Republic of China
Charles University, Ovocnytrh 5, Praha 1, 116 36, Prague, Czech Republic
Czech Technical University, Zikova 4, 166 36 Prague 6, Czech Republic
Institute of Physics, Academy of Sciences of the Czech Republic, Na Slovance 2,
182 21 Prague 8, Czech Republic
Helsinki Institute of Physics and University of Jyväskylä, P.O.Box 35, FI-40014 Jyväskylä, Finland
Dapnia, CEA Saclay, F-91191, Gif-sur-Yvette, France
Laboratoire Leprince-Ringuet, Ecole Polytechnique, CNRS-IN2P3, Route de Saclay,
F-91128, Palaiseau, France
Laboratoire de Physique Corpusculaire (LPC), Université Blaise Pascal, CNRS-IN2P3,
Clermont-Fd, 63177 Aubiere Cedex, France
IPN-Orsay, Universite Paris Sud, CNRS-IN2P3, BP1, F-91406, Orsay, France
Debrecen University, H-4010 Debrecen, Egyetem tér 1, Hungary
ELTE, Eötvös Loránd University, H - 1117 Budapest, Pázmány P. s. 1/A, Hungary
KFKI Research Institute for Particle and Nuclear Physics of the Hungarian Academy of Sciences (MTA KFKI RMKI),
H-1525 Budapest 114, POBox 49, Budapest, Hungary
Department of Physics, Banaras Hindu University, Varanasi 221005, India
Bhabha Atomic Research Centre, Bombay 400 085, India
Weizmann Institute, Rehovot 76100, Israel
Center for Nuclear Study, Graduate School of Science, University of Tokyo, 7-3-1 Hongo, Bunkyo,
Tokyo 113-0033, Japan
Hiroshima University, Kagamiyama, Higashi-Hiroshima 739-8526, Japan
Advanced Science Research Center, Japan Atomic Energy Agency, 2-4 Shirakata Shirane, Tokai-mura,
Naka-gun, Ibaraki-ken 319-1195, Japan
KEK, High Energy Accelerator Research Organization, Tsukuba, Ibaraki 305-0801, Japan
Kyoto University, Kyoto 606-8502, Japan
Nagasaki Institute of Applied Science, Nagasaki-shi, Nagasaki 851-0193, Japan
RIKEN, The Institute of Physical and Chemical Research, Wako, Saitama 351-0198, Japan
Physics Department, Rikkyo University, 3-34-1 Nishi-Ikebukuro, Toshima, Tokyo 171-8501, Japan
Department of Physics, Tokyo Institute of Technology, Oh-okayama, Meguro, Tokyo 152-8551, Japan
Institute of Physics, University of Tsukuba, Tsukuba, Ibaraki 305, Japan
Chonbuk National University, Jeonju, South Korea
Ewha Womans University, Seoul 120-750, South Korea
Hanyang University, Seoul 133-792, South Korea
KAERI, Cyclotron Application Laboratory, Seoul, South Korea
Korea University, Seoul, 136-701, South Korea
Accelerator and Medical Instrumentation Engineering Lab, SungKyunKwan University,
53 Myeongnyun-dong, 3-ga, Jongno-gu, Seoul, South Korea
Myongji University, Yongin, Kyonggido 449-728, Korea
Department of Physocs and Astronomy, Seoul National University, Seoul, South Korea
Yonsei University, IPAP, Seoul 120-749, South Korea
IHEP Protvino, State Research Center of Russian Federation, Institute for High Energy Physics,
Protvino, 142281, Russia
INR_RAS, Institute for Nuclear Research of the Russian Academy of Sciences, prospekt 60-letiya Oktyabrya 7a,
Moscow 117312, Russia
Joint Institute for Nuclear Research, 141980 Dubna, Moscow Region, Russia
Russian Research Center "Kurchatov Institute", Moscow, Russia
PNPI, Petersburg Nuclear Physics Institute, Gatchina, Leningrad region, 188300, Russia
Saint Petersburg State Polytechnic University, St. Petersburg, Russia
Skobeltsyn Institute of Nuclear Physics, Lomonosov Moscow State University, Vorob'evy Gory,
Moscow 119992, Russia
Department of Physics, Lund University, Box 118, SE-221 00 Lund, Sweden
July 2012