## Slide 1: sPHENIX Local Level 1 Review
Overview
Hardware
Algorithm
  EMCAL data processing, Jet, Pair
L1 latency discussion
Data Alignment issue
FPGA flash memory.
Test data/monitor
Hardware modification
More stuffs to be done.

## Slide 2: Calorimeter Level 1 trigger
Receive trigger primitives from
  EMCAL has 96(eta) X 256 (phi) channels, 0.025 eta and phi
  HCAL 1536 each, =24x64 channels (per inner or outer HCAL) 0.1 eta and 0.1 phi
  MBD 128 channel, charge and time measurements
  These systems use calorimeter digitizer module (64 channel per module) as front end module.
Generate
  Send possible Pair trigger, Jet trigger and interaction trigger (MBD) candidate to Global Level 1 trigger
FEMs
Local Level 1 trigger
Global Level
1 Trigger

## Slide 3: Issues
Local level 1 trigger is strange system to prove it works
  It is not practical to test system as whole
    Too many inputs, have to test slice by slice….
  Hardware
    Is system design meet the running requirements??
    How can we proven the system works??
      Make sure input and outputs works
  Firmware
    Can we the FPGA design meet the 1st cut physics requirements??
      Pair trigger
      Jet trigger
      MBD interaction trigger
  Resource management
    How many bits can fit into one fiber??
    How many fibers one can stuffs into one FPGA.
    How much resources inside FPGA…

## Slide 4
FEM
256 channel in phi
8x8
channel
96 channel
cross
stitching
cross
stitching
The EMCAL dominates the channel counts  24,576
overlapping sum  neighbor problem
Choose a complete z section slice, will grabbing data from neighbor slices.
Slice needs to be wide enough to reduce the cross stitching problem
Each 64 channel -> 1 optical fibers
Map 24 input fibers to 1 FPGA..
16 (phi) X 96 (z)
HARDWARE CHOICE

## Slide 5
receiver
Cross stitch
Overlap 2x2 of 2x2 sum
Peak
finder
8x8 sum
receiver
inner/outer HCAL
2x2 sum
EMCAL
HCAL
Pair trigger
JET trigger
receiver
Interaction window / charge
GL 1
MBD
LL1 Block Diagram
FEM
FEM
FEM

## Slide 6
EMCAL
L1 data
processor
(inner/outer)
HCAL data
Concentrator
EMCAL
L1 data
processor
EMCAL
L1 data
processor
16 fibers
16 fibers
16 fibers
Pair Trigger
JET Trigger
24
24
24
24
Global
Level 1
Shower Max
8x8 sum
non-overlapped
24
LL1 data
(JSEB II)
(20 optical links)
crate backplanes
(slow control/timing)
LL1 triggered
Summary data
Reduced
Trigger
Data
Reduced
Trigger
Data

## Slide 7
3 12 ports
receivers
12 ports
transmitter
Download
path
Readback
path
Reference
crystal
Altera
Arria 10
FPGA
2.5V/3.3V
optical
2.5V
0.95V
0.9V
1.8V
+12V
in
+12V
in
6x
clock
Mode
Bit in
FLASH
Memory
sPHENIX Trigger Board
Build block for local level 1 system
Hosted in the calorimeter digitizer crate
  Provide slow control/readback paths
  Receive 6x clocks and mode bit (L0 and L1 trigger)
  Provide 12V input power
    Can not be used together with digitizer board, upper 12V power.
Board size 6U X 190 mm
Supply 12V around 3A
Two reference clocks crystals.
  120 MHz FEM link and 156.25 MHz for GL1 & Monitor (JSEBII).
2 building blocks
  Each block
    36 receivers + 12 transmitters
    1 Arria 10 FPGA
2 half modules + 1 full module assembled.

## Slide 8: Digitizer Crate
The Calorimeter digitizer crate system provides
  Interface with GTM through clockmaster Module
    Timing and L0, L1 timing information
  Slow control download and readback
  Mechanical support
  Power entry…

## Slide 9: The Digitizer Subsystem Technical Overview
Controller
clockmaster
GTM
JSEB II
PC
ADC
ADC
XMIT
Trigger
out
Trigger
out
DCM II
crate
(rack based)
Slow control/readback
Beam clock,
L0, L1 trigger
SPHENIX DAQ System
detector
Slow control/readback
bus, L0, L1 trigger
Token passing
dataway
Token passing
dataway
Clock are fanout point to
point through the backplane
Crate based system.
Signals are cable from the on-detector electronics.
Digitized with 14 bit ADC.
Receive timing information the SPHENIX Granule Timing Module (GTM)
Generate L1 trigger primitives
Receive L1 trigger and send out L1 triggered event data to Data Collection Module II (DCMII).
Provide buffer for both the 40 beam crossing L1 delay buffer and 4 L1 triggered events
3 ADC  XMIT
3Gbit/sec
optical link
1.6Gbit/sec
optical link

## Slide 10: Arria 10 FPGA
20nm technology, 10AX570N4NF40I3G
48 transceivers, 6 Gbps upper limit.
570K logic elements  868K registers
1800 20Kbits memory block  35 Mbits
3000 18x19 multipliers.
  Mostly useless for our application…
Core voltage  0.9V, transceiver voltage  0.95V, I/O voltage  1.8V, 2.5V for optical interface.
Transceiver block is separated from core block.
  Easy routing

## Slide 11: Optical ports
Avago/Foxconn/Broadcom 12 port transmitter/receiver
  AFBR-814/AFBR_824 (MiniPot)
Plug in module, size 21.95mmx 18.62mm
Optical wavelength 850nm – up to 150 meter with OM4 4700 Mhz-km fiber.
Up to 10 Gbits/sec
Use 2.5V and 3.3V
Use light turn connector cable  MPO outside
  12 fibers
  Use flat cable
Last order data 3/18/2021
  No replacement alternative…

## Slide 12
100 ohms terminations
3.6 Gbps
100 ohms terminations
2.4 Gbps Gbps
Differential probe at the receiver

## Slide 13
JSEB II
(PCIE)
controller
EPLD
ECC encoder
ECC decoder
transmitter
receiver
receiver
receiver
FEM
ECC encoder
Test both 2.4 Gbps and 4.8 Gbps through Transmitter  receiver loopback
  Through 1000 words packet, random number.
  Over 20M+ packets on some board on full board, no error
  Over 1+M packets on all the ports, no error with ECC detection
    1 M packet = 106X103X16 = 1.6X1010 bits.
Tested FEM  L1 trigger prototype module
  1000 words packet, random number.
  Over 2+M packets, NO ECC errors (recovered or fatal error) with ECC correction.
Optical Port Test
2.4 Gbps is done through 16 bits word Altera
Transceiver interface.
4.8 Gbps is done through 32 bits word Altera
Transceiver interface.

## Slide 14
Optical
receiver
Stitching/
alignment
Overlap
4x4 sum
8x8 SUM
Peak
finding
Priority
encoding
sorting
EMCAL processing flow
Neighbor
slice
Neighbor
slice

## Slide 15
7X ADC clock
F
R
A
M
E
Serialized ADC DATA
De-serializer
Serial
command
L1
Delay
Buffer
5 L1
Accepted
Event
buffer
Token
Passing
Data
ALTERA Arria V GX
BB1D4F35
1152 pins FPGA
Analog
Device
AD9257
8 channel
14bits
65 MHz
ADC
Clock
Fanout
Differential
receiver
6 X beam
clock
2 mm
Hard Metric
Analog
Device
AD9257
8 channel
14 bits
65 MHz
ADC
2 mm
Hard Metric
Differential
receiver
Serialized ADC DATA
F
R
A
M
E
7X ADC clock
64 channel
ADC board
6x beam clock
Beam phase,
init, L1
Serialized
Token
Passing
command/
offline data read
De-serializer
Bused command
Serial data
+- 3.5V, -2.5V
Differential
receiver power
+1.8V analog
ADC power
+1.8V digital
ADC power
DC/DC
switch regulator
+4V, -3.5V, +2.5V
Power
+12V
Power
DC/DC
switch regulator
1.5V
LDO
1.1V
core
4V
2.5V FPGA I/O
3.3V
LDO
3.3V
LDO
D
P
U
two transceivers
two transceivers
sPHENIX ADC Module Block Diagram
L1 trigger primitives
transceiver out
RHIC beam clock 9.6MHz

## Slide 16
Baseline
subtraction
Read address = write address -delay
Delay a parameter
Probably has 2 clocks offset
Dual port memory
Lookup memory
(1024X10)
Read
Address
(upper 10 bits)
Sub = ADC – ADCpre
If (adcpre > adc) sub=0
Load lookup
Memory from
Slow control
10 bits
2X2 SUM
(12 bits output)
only use
upper 8 bits
Choose one of the of of the 12X BC clock phas for trigger primitive
64 channels
16 2X2 8 bits sum
6X BC clock
12X BC Clock
MUX
128 bits
To 8 16 bits
120 MHz clock
10X16 bits FIFO
Transceiver
IP
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
header | Mod + clock | Sum 1+2 | Sum 3+4 | Sum 5+6 | Sum 7+8 | Sum 9+10 | Sum 11+12 | Sum 13+14 | Sum 15+16
delay
+1
+2
+1
+ 1 BC + 2 12X
4 bits trigger phase
Cal trigger primitive Generator (preliminary)
Monitor Delay dual port memory
5 events buffer
L1
trigger
To controller
readout
Delay and
# of Sample
adjustable

## Slide 17
MBD Trigger Primitive data path (preliminary)
ADCs
Post-Pre
Timing
Block
ADCs
Post-Pre
10X10 lookup table
10X10 lookup table
Choose
phase
Choose
phase
Slewing
Correction
12X9
9 bits
3 bits
Time
SUM
Charge
SUM
7 bits
6X beam clock
Time
channels
charge
channels
Trigger
output
2.5 Gbps
8 X16 bits words per beam crossing
optics
ADC clock and discriminator clock are interlock together.. So sample height is fixed for a given PMT pulse time
Beam gate is 25ns  9 bits range will be 50ps per division.
For the timing block we can choose either fix sample relative to BC, peak finder etc…
For 32
channels

## Slide 18
Wide FIFO
Demux
optical
Transmitter
IP
Optical
Receiver
IP
FIFO
mux
Wide Register
input data
Processed
data
lst
Processing
clock
TX reference
clock
RX reference
clock
processing block
clock
Fill frame
data
data
data
data
header
Fill frame
Generic Optical Data Flow Diagram
Generic Data format
Write
(sync)
read
(!empty)

## Slide 19
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  | 2 |  |  |  | 3 |  |  |  | 4 |  |  |  | 5 |  |  |  | 6 |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 3 | 1 4 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 2 4
Beam clock (BC)
6 X BC
24 X BC
1
BC ~ 9.6 MHz
120 MHz
Optical
Reference
clock
24X BC (short hand as clock240)  is generated from 6X BC (short hand as clock60)
Beam clock phase is derived from serialized mode bits. 6X BC is the clock from GTM.
Clock240  system clock for trigger calculation.
Phase bit counter is the drive from the edge of BC with clock240 clock.
Slow control set phase bit counter value to generated “SYNC” bits
Slow control is driven slow control clock from the controller (~3XBC)
Trigger Module Clocks

## Slide 20
Dual port memory
(64X3081)
sync
bc,sync
data
3081 = 8 (phi) * 48 (eta) * 8 bits + BC count (8) + sync (1)
Read address =
Write address -delay
Alignment register
Sync out
2x2 sums from
neighbor trigger blocks
Cross stitching Align data block
2x2 sum data is aligned from all inputs.
data is stable for entire BC clock period.

## Slide 21
48 in eta
11 in phi
8 in phi
Calorimeter L1 trigger FPGA slide , 24 FEM cover 8 phi slice and complete eta space.
(2x2 sum map)

## Slide 22
03 | 13 | 23 | 33
02 | 12 | 22 | 32
01 | 11 | 21 | 31
00 | 10 | 20 | 30
2x2 sum
Generate over lapped 4x4 sum
From 11X 48 (phi, eta) 8 bits 2x2
 10 X47 10 bits 4x4 sum
 8 in phi and 45 in phi peak finder cell
(valid bit high if SUM > threshold)
02 | 12 | 22
01 | 11 | 21
00 | 10 | 20
d
d
> | > | >
>= | SM | >
>= | >= | >
2x2 SUM
Overlapped
4x4 sum
Peak finding
If SUM > threshold (common),
Valid =high
Peak finding
Based on
Over-lapped
4x4 sum
Peaking finding

## Slide 23
48 in eta
11 in phi
8 in phi
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
12 | 13 | 14 | 15
8 | 9 | 10 | 11
4 | 5 | 6 | 7
0 | 1 | 2 | 3
2x2 sum
ordering
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
overlapped data to
neighbor slide

## Slide 24: Sorting procedure
After peak finding algorithm, a single phi slide of overlapped 4x4 sum is 45 wide array.
  The tower sum pass the threshold is represented in the valid bit array, valid bit =1
Expend the 45 wide array to 48 wide array i.e.
  valid[0:48] = 1’b0, valid[0:44], 2’b0
Using the Valid bit array and sum value to convert 2 dimension of tower array to a list of the peaks value through
  1) priority encoding
  2) sorting

## Slide 25
1 | 2 | 3
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
A Phi slice of
peak
Priority encoding method:
1) go through valid bit
1) Cut phi slide into 3 groups, each group 16 channel
2) check with group 1 to see all bits are zero.
if not empty, encode the bit location to 4 bit address start from lowest order channel
till all non zero bits are encoded
if Yes, go to group 2
4) repeat the procedure for group 2 then group 3
5) output the result as list of peak sum and address. Maximum 4 hits per slice
Priority Encoding

## Slide 26
Merging routine
sort
sort
sort
sort
sort
sort
8 phi slices after priority encoding
4 hits per slices
Sort 8 hits
Top 4 hits
Optical out
(8 (8 bits address, 10 bits sum) + 7 bits ID + 8 bit BC + 1 empty bit)
Optical out
(8 (8 bits address, 10 bits sum) + 7 bits ID + 8 bit BC + 1 empty bit)
To avoid the two peak sum value is the same. The data is shift left by one bits.
If the sum is equal add 1 to the sum, start from the top of the array

## Slide 27
48 in eta
11 in phi
8 x 8 sum
Optical out
1
Optical
Out
2
8x8 sum  optical out
12 of 12 bits sum value
7 bit header, 8 bits BC counter, 1 empty bit
(2x2 sum map)

## Slide 28: slide window 10 optical port summery
24 input ports from FEM directory
  2.4 Gbits/sec, 8 phi slice.
6 cross stitching input ports
  3.84 Gbits/sec, 3 phi slice, 24 2x2 sum per link.
    3.84 Gbits/sec. Maximum 18 16 bits words  16 data words  32 2x2 SUMs
6 cross stitching output ports
  3.84 Gbits/sec, 3 phi slice, 24 2x2 sum per link.
2 output ports for emcal 8x8 sum
  This has to be reduce to 1 port ???
    24 8 bits words + 1 16 bits header words
2 output ports for show max.
  Need to reduce to 1 output port.
    Depend on how many candidates after sorting.

## Slide 29: Jet trigger
16 optical inputs from EMCAL section
16 optical inputs from HCAL section
Data is organized as 8x8 sum from EMCAL (0.2 eta X0.2 phi)
  Group into 32 (256/8) X 12 (96/8) array.
Data is organized as 2x2 sum from HCAL (0.2 eta X0.2 phi)
  This is done from FEM
  Concentrator is needed to pack outer HCAL 24 fibers into 16 fibers
    add inner HCAL with outer HCAL.
    FEM optical bandwidth 2.4 Gbps.

## Slide 30
32 in phi
12 in eta
8 x 8 sum maps
when deal with overlapped 4x4 sum (0.8 eta X 0.8 phi) based on the <8X8> sum
done to find jet peak
extend 1st 3 phi columns to larger phi area  convert cylinder to 2D space.

## Slide 31: Pair trigger
16 optical inputs.
  Each FEM cover 16 phi X 96 eta. Further divide into 2 slice, 8X96.
    The optical data is organized into 3 possible pairs per slices.
      One valid indicates slice has non-zero 1st data in array (at least one data is above zero)…
      8 bit address, 10 bits data
        Need to find 8 bit address sub field.
      4 bits phi address will be added to identify the FEM sub address.

## Slide 32
Pair Search Path
Phi project view
The phi section is cut into 32 sections.
The pair search path range is +- 1 sections
A new valid bit is created with the possible search.
for example x[0] = v[0] & (v[15] | v[16] | v[17]);
v[x], x= section number.
The priority encoding is done based on the new valid bit.
it generate 12 possible match pairs.
Based the possible match pairs
for each possible pairs 3 hits per phi position X 3 possible opposite connection X 3 hits per connection => 27 possible pairs.

## Slide 33
Pair mass calculation
HIT:
Energy  10 bits
Phi  7 bits 16 fibers, 2 sub division per fiber, 8 bits address per fiber. < 2bits on phi>
Eta  6 bits
Mass calculation use
upper 3 bits of eta
upper 3 bits of phi ( this probably a mistake) .. The important parts is phi1 – phi2
all 10 bits of energy
Look up table
12 bits address ( 2 pair’s angle ) with 8 bits output
10 bits multiplier with 20 bits output
Energy 1 X Energy 2
Square Root of E1X E2
Multiplier of 8 bits X 10 bits
Mass cut is done through upper and low mass limits. The limits is loaded by slow control.

## Slide 34: Pair trigger output
If any one of the 27 pairs, pass the mass cut. The Mass value is send out via optical data
  One bit indicate mass pass the cut.
There are 12 possible hits through pair finding algorithm.
The trigger output is send out via 2nd reference clock crystal.
  156.25 MHz

## Slide 36
The transmitter start at 1598.. The receiver start at 1622. The difference is 24.
The clock is tx_out, 120 MHz. clock period 8.333ns.
The delay is ~200 ns…
Signal Tap picture for the L1 trigger loopback test.

## Slide 37
ADC
De-serializer
FIFO
Post-pre
(ADC)
(FIFO)
FEM FPGA
10 bits X 8 lookup
2x2 channel
sum
drop
Lower
4 bits
Pick trigger
phase
Form
Trigger packet
Optical transmitter
Optical receiver
LL1
100ns per division.
6x BC ~ 60 MHz
120 MHz
Crystal
Clock
16 clocks
latency
FIFO
PRELIMINARY

## Slide 38
LL1
receiver
FIFO
Data re-Map
FIFO
Edge
Transmitter
Edge
receive
FIFO
3.84 Gbps
24X BC ~ 240 MHz
450ns (108 counts with 240 MHz clock)
Calorimeter EMCAL cross stitching
Delay memory
Alignment
pulse
PRELIMINARY

## Slide 39: Data alignment
Three alignment stages
  Data alignment on the FEMs side
    In 16ns steps, 1 or 2 steps
    Adjustment delay steps in the FEM. (not implemented yet)
  Alignments on the EMCAL calorimeter inputs
    Alignment after cross stitching.
  Adjustment inside the Calorimeter trigger module
    Not per FEM link

## Slide 40
Beam
diamond
Sampling clock
uncertainty
Cable
delay
data
hold
Transfer
to trigger
Shower max window
Shower max window
BC
BC
BC
BC
BC
BC
BC
6x beam clock
FEM Alignment

## Slide 41: Trigger FPGA Code Loading
The Trigger board FPGA is loaded through on board 512 MB Flash memory.
  Arria 10X570 configuration need 255 Mbits if configuration data is not compressed.
  Direct programming of flash memory is through Altera programmer.
    Load FPGA factory code  read/write the flash memory through factory code.
  Although it is not tested yet, the flash memory should be able to program through slow control and Altera IP core.
    It is the same method as digitizer flash memory programming method.

## Slide 42: Test data/Monitoring
We have two independent data paths from the trigger data flow
  Slow control download/readback path.
    Loading test data etc./readback system status
  Readout path to JSEB II.
    Untested. It use the unused transmitter, receiver(??)
It is not possible to even readout fraction of input data stream into the monitor system
  We will use the slow control to issue command, then sample of data stream will be load into registers. We will read the content of the registers.
The test data can be used in the offline mode.

## Slide 43: Board modification
There are few things need to be done for the next generation
  The cooling heat sink + fan
    System can run without cooling fan+ heat sink. But it will heat up quickly without crate fan
    It will be attached standard Thermal adhesive. It is too difficult to add machinical constrain.
    Add +12V Fan power entry point near the fuse.
  Add one address bit for upper and lower FPGA.
  Add couple LED.
Except for LED, the Fan power and address bit are already add to prototype board.

## Slide 44: Things need to be done
Need confirm our optical communication with JSEB2.
  Also going to be used for the GL1 Link.
Need to firm up the L1 latency.
  We can use pair trigger + emcal processing block to do this measurement
  Except for the optical delay, the processing cycle contribute to the L1 latency is smaller.
Firm up the LL1 to GL1 communication.
  The LL1 output…