## Slide 1: Understand local level 1 (LL1) trigger
The LL1 is making decision every beam crossing based the FEMs data on the with fixed latency.
  This implies we have to use subset of the FEM data.
    The full FEM data is 64 channel x 14 bits x ~10 MHz = ~8 Gbits/sec of raw data.
The calorimeter LL1 need to
  Organize data to be processed.
    Map data into match calorimeter
  Process data in parallel and in pipeline.
  Reduce subset of FEM data in something manageable.
    Turn 2D problem into 1D issue
  Because of overlapping sum requirement, we could
    Put all the data into one FPGA or
    Make sure sub-set of data are group together, copy data from one region to another region.
  Building EMCAL LL1 trigger primitives
    For pair physics trigger, peak finder for overlapping 2x2 sum out of 2x2 sum from FEM
    For jet physics trigger, 4x4 sum out of 2x2 sum from FEM.
  For HCAL
    Re-organize data, add inner and outer HCAL together.
  For MBD
    Collect data, perform a divide fuction1111

## Slide 2: Calorimeter Level 1 trigger
Receive trigger primitives from
  EMCAL has 96(eta) X 256 (phi) channels, 0.025 eta and phi
  HCAL 1536 each, =24x64 channels (per inner or outer HCAL) 0.1 eta and 0.1 phi
  MBD 128 channel, charge and time measurements
  These systems use calorimeter digitizer module (64 channel per module) as front end module.
Generate
  Send possible Pair trigger, Jet trigger, Cosmic ray trigger and interaction trigger (MBD) candidate to Global Level 1 trigger,
FEMs
Local Level 1 trigger
Global Level
1 Trigger

## Slide 3
3 12 ports
receivers
12 ports
transmitter
Download
path
Readback
path
Reference
crystal
Altera
Arria 10
FPGA
2.5V/3.3V
optical
2.5V
0.95V
0.9V
1.8V
+12V
in
+12V
in
6x
clock
Mode
Bit in
FLASH
Memory
sPHENIX Trigger Board
Build block for local level 1 system
Hosted in the calorimeter digitizer crate
  Provide slow control/readback paths
  Receive 6x clocks and mode bit (L0 and L1 trigger)
  Provide 12V input power
    Can not be used together with digitizer board, upper 12V power.
Board size 6U X 190 mm
Supply 12V around 3A
Two reference clocks crystals.
  120 MHz FEM link and 156.25 MHz for GL1 & Monitor (JSEBII).
2 building blocks
  Each block
    36 receivers + 12 transmitters
    1 Arria 10 FPGA
2 LEMO outputs
One LED
LEMO
out

## Slide 4
EMCAL
L1 data
processor
(inner/outer)
HCAL data
Concentrator
EMCAL
L1 data
processor
EMCAL
L1 data
processor
16 fibers
16 fibers
16 fibers
Pair Trigger
JET Trigger
24
24
24
24
Global
Level 1
Shower Max
8x8 sum
non-overlapped
24
crate backplanes
(slow control/timing)
LL1 triggered
Summary data
Reduced
Trigger
Data
Reduced
Trigger
Data
MBD
Trigger
2
2

## Slide 5
receiver
Cross stitch
Overlap 2x2 of 2x2 sum
Peak
finder
8x8 sum
receiver
inner/outer HCAL
2x2 sum
EMCAL
HCAL
Pair trigger
JET trigger
receiver
Interaction window / charge
GL 1
MBD
LL1 Block Diagram
FEM
FEM
FEM
Cosmic trigger

## Slide 6: LL1 data path
The LL1 has 3 data streams
  The input stream from FEM or adjacent trigger block or upstream LL1 trigger block
  The output stream to adjacent trigger block or downstream LL1 trigger block or GL1 input
  The data monitor output to either JSEB II or crate controller.
    We can monitor subset of data via LL1 trigger event.
      Instead of ~10 MHz beam clock rate, we now reduce to maximum 12.5 KHz L1 trigger rate.
The control path is from crate controller.
  Loading parameters
The LL1 clock input is from GTM through crate controller.
  Faster processing clock is generated through phase lock loop.

## Slide 7: Front End Electronics (ADC)

## Slide 8
7X ADC clock
F
R
A
M
E
Serialized ADC DATA
De-serializer
Serial
command
L1
Delay
Buffer
5 L1
Accepted
Event
buffer
Token
Passing
Data
ALTERA Arria V GX
BB1D4F35
1152 pins FPGA
Analog
Device
AD9257
8 channel
14bits
65 MHz
ADC
Clock
Fanout
Differential
receiver
6 X beam
clock
2 mm
Hard Metric
Analog
Device
AD9257
8 channel
14 bits
65 MHz
ADC
2 mm
Hard Metric
Differential
receiver
Serialized ADC DATA
F
R
A
M
E
7X ADC clock
64 channel
ADC board
6x beam clock
Beam phase,
init, L1
Serialized
Token
Passing
command/
offline data read
De-serializer
Bused command
Serial data
+- 3.5V, -2.5V
Differential
receiver power
+1.8V analog
ADC power
+1.8V digital
ADC power
DC/DC
switch regulator
+4V, -3.5V, +2.5V
Power
+12V
Power
DC/DC
switch regulator
1.5V
LDO
1.1V
core
4V
2.5V FPGA I/O
3.3V
LDO
3.3V
LDO
D
P
U
two transceivers
two transceivers
sPHENIX ADC Module Block Diagram
L1 trigger primitives
transceiver out
RHIC beam clock 9.6MHz

## Slide 9
Baseline
subtraction
Read address = write address -delay
Delay a parameter
Probably has 2 clocks offset
Dual port memory
Lookup memory
(1024X10)
Read
Address
(upper 10 bits)
Sub = ADC – ADCpre
If (adcpre > adc) sub=0
Load lookup
Memory from
Slow control
10 bits
2X2 SUM
(12 bits output)
only use
upper 8 bits
Choose one of the of of the 12X BC clock phas for trigger primitive
64 channels
16 2X2 8 bits sum
6X BC clock
12X BC Clock
MUX
128 bits
To 8 16 bits
120 MHz clock
10X16 bits FIFO
Transceiver
IP
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
header | Mod + clock | Sum 1+2 | Sum 3+4 | Sum 5+6 | Sum 7+8 | Sum 9+10 | Sum 11+12 | Sum 13+14 | Sum 15+16
delay
+1
+2
+1
+ 1 BC + 2 12X
4 bits trigger phase
Cal trigger primitive Generator (preliminary)

## Slide 10
MBD Trigger Primitive data path (preliminary)
ADCs
Post-Pre
Timing
Block
ADCs
Post-Pre
10X10 lookup table
10X10 lookup table
Choose
phase
Choose
phase
Slewing
Correction
12X9
9 bits
3 bits
Time
SUM
Charge
SUM
7 bits
6X beam clock
Time
channels
charge
channels
Trigger
output
2.5 Gbps
8 X16 bits words per beam crossing
optics
ADC clock and discriminator clock are interlock together.. So sample height is fixed for a given PMT pulse time
Beam gate is 25ns  9 bits range will be 50ps per division.
For the timing block we can choose either fix sample relative to BC, peak finder etc…
For 32
channels

## Slide 11
Wide FIFO
Demux
optical
Transmitter
IP
Optical
Receiver
IP
FIFO
mux
Wide Register
input data
Processed
data
lst
Processing
clock
TX reference
clock
RX reference
clock
processing block
clock
Fill frame
data
data
data
data
header
Fill frame
Generic Optical Data Flow Diagram
Generic Data format
Write
(sync)
read
(!empty)

## Slide 12
1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  | 2 |  |  |  | 3 |  |  |  | 4 |  |  |  | 5 |  |  |  | 6 |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 1 3 | 1 4 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 2 4
Beam clock (BC)
6 X BC
24 X BC
1
BC ~ 9.6 MHz
120 MHz
Optical
Reference
clock
24X BC (short hand as clock240)  is generated from 6X BC (short hand as clock60)
Beam clock phase is derived from serialized mode bits. 6X BC is the clock from GTM.
Clock240  system clock for trigger calculation.
Phase bit counter is the drive from the edge of BC with clock240 clock.
Slow control set phase bit counter value to generated “SYNC” bits
Slow control is driven slow control clock from the controller (~3XBC)
Trigger Module Clocks

## Slide 13: MBD LL1 trigger

## Slide 14
 | MBD FEM  LL1 Data Packet
Bit 8 - 0 | Charge Sum channel 3-0
Bit 17 - 9 | Charge Sum channel 7-4
Bit 26 - 18 | Charge Sum channel 11 - 8
Bit 35 - 27 | Charge Sum channel 15 - 12
Bit 44 - 36 | Charge Sum channel 19 - 16
Bit 53 - 45 | Charge Sum channel 23 - 20
Bit 62 - 54 | Charge Sum channel 27 - 24
Bit 71 - 63 | Charge Sum channel 31 - 28
Bit 79 - 72 | 2’b0, nhit(5:0)
Bit 91 - 80 | Time Sum channel 7 - 0
Bit 103 -92 | Time Sum channel 15 - 8
Bit 115 - 104 | Time Sum Channel 23 - 16
Bit 127 - 116 | Time Sum channel 31 - 24
Bit 143 - 128 | Header word

## Slide 15
Time sum
8 channeld
Time SUM
Time sum
8 channel
Mod 0 ch7-0
Mod 1 ch31-24
nhit
Mod 0
nhit
Mod 1
Total hits
divide
Time Average
Time sum
8 channeld
Time SUM
Time sum
8 channel
Mod 2 ch7-0
Mod 3 ch31-24
nhit
Mod 2
nhit
Mod 3
Total hits
divide
Time Average
MBD LL1 trigger
processing block

## Slide 16: Calorimeter triggers

## Slide 17
FEM
256 channel in phi
8x8
channel
96 channel
cross
stitching
cross
stitching
The EMCAL dominates the channel counts  24,576
overlapping sum  neighbor problem
Choose a complete z section slice, will grabbing data from neighbor slices.
Slice needs to be wide enough to reduce the cross stitching problem
Each 64 channel -> 1 optical fibers
Map 24 input fibers to 1 FPGA..
16 (phi) X 96 (z)
HARDWARE CHOICE
EMCAL/HCAL topology
TURN cylinder to 2D MAP

## Slide 18: HCAL data concentrator
The HCAL detector has 24 FEM each (24 fibers)
LL1 has 36 optical fiber inputs, not enough to cover inner + outer detectors.
Split the detectors to half, one half per LL1 trigger block.
Treat the inner and outer detectors together.
  Add inner + outer detectors trigger sum and divide by factor 2.

## Slide 19
E
T
A
PHI (180 degree)
2x2
4 FEMS
3 FEMS
2 2X2 in eta
16 2X2 in phi
2 2X2 in eta
16 2X2 in phi
Lkup add
Lkup add
(“OR” of 2x2 sum>= thres)
(“OR” of 2x2 sum>= thres)
Output to jet
Physics trigger
Inner and outer are added
HCAL data concentrator
block diagram
Outer and inner
detectors are treat
Separately
6 bits each

## Slide 20
12X1 look up table
6 bits inner
6 bits outer
One bit output
Cosmic ray trigger
HCAL cosmic ray trigger block

## Slide 21: EMCAL (data concentrator)

## Slide 22
Optical
receiver
Stitching/
alignment
Overlap
4x4 sum
8x8 SUM
Peak
finding
Priority
encoding
sorting
EMCAL processing flow
Neighbor
slice
Neighbor
slice

## Slide 23
From Jet trigger, EMCAL will do 4x4 non-overlaping sum out of 2x2 sum
  Each of 4x4 sum  0.2 x 0.2 eta and phi.
HCAL channel cover 0.1 x 0.1 eta and phi
  HCAL 2x2 sum cover 0.2X0.2 eta and phi

## Slide 24
48 in eta
11 in phi
8 in phi
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
12 | 13 | 14 | 15
8 | 9 | 10 | 11
4 | 5 | 6 | 7
0 | 1 | 2 | 3
2x2 sum
ordering
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
FEM
(8X8)
64 channel
overlapped data to
neighbor slide

## Slide 25: Pair trigger preparation

## Slide 26
Dual port memory
(64X3081)
sync
bc,sync
data
3081 = 8 (phi) * 48 (eta) * 8 bits + BC count (8) + sync (1)
Read address =
Write address -delay
Alignment register
Sync out
2x2 sums from
neighbor trigger blocks
Cross stitching Align data block
2x2 sum data is aligned from all inputs.
data is stable for entire BC clock period.

## Slide 27
8x48 2x2 sum (24 fibers)
11x48 2x2 sum (LL1 block)
1 Jet trigger out
2 pair trigger out
4 RX
2 TX
2 RX
4 TX
1 monitor out

## Slide 28
48 in eta
11 in phi
8 in phi
Calorimeter L1 trigger FPGA slide , 24 FEM cover 8 phi slice and complete eta space.
(2x2 sum map)

## Slide 29
03 | 13 | 23 | 33
02 | 12 | 22 | 32
01 | 11 | 21 | 31
00 | 10 | 20 | 30
2x2 sum
Generate over lapped 4x4 sum
From 11X 48 (phi, eta) 8 bits 2x2
 10 X47 10 bits 4x4 sum
 8 in phi and 45 in phi peak finder cell
(valid bit high if SUM > threshold)
02 | 12 | 22
01 | 11 | 21
00 | 10 | 20
d
d
> | > | >
>= | SM | >
>= | >= | >
2x2 SUM
Overlapped
4x4 sum
Peak finding
If SUM > threshold (common),
Valid =high
Peak finding
Based on
Over-lapped
4x4 sum
Peaking finding

## Slide 30: Sorting procedure
After peak finding algorithm, a single phi slide of overlapped 4x4 sum is 45 wide array.
  The tower sum pass the threshold is represented in the valid bit array, valid bit =1
Expend the 45 wide array to 48 wide array i.e.
  valid[0:48] = 1’b0, valid[0:44], 2’b0
Using the Valid bit array and sum value to convert 2 dimension of tower array to a list of the peaks value through
  1) priority encoding
  2) sorting

## Slide 31
1 | 2 | 3
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
A Phi slice of
peak
Priority encoding method:
1) go through valid bit
1) Cut phi slide into 3 groups, each group 16 channel
2) check with group 1 to see all bits are zero.
if not empty, encode the bit location to 4 bit address start from lowest order channel
till all non zero bits are encoded
if Yes, go to group 2
4) repeat the procedure for group 2 then group 3
5) output the result as list of peak sum and address. Maximum 4 hits per slice
Priority Encoding

## Slide 32
Merging routine
sort
sort
sort
sort
sort
sort
8 phi slices after priority encoding
4 hits per slices
Sort 8 hits
Top 4 hits
Optical out
(8 (8 bits address, 10 bits sum) + 7 bits ID + 8 bit BC + 1 empty bit)
Optical out
(8 (8 bits address, 10 bits sum) + 7 bits ID + 8 bit BC + 1 empty bit)
To avoid the two peak sum value is the same. The data is shift left by one bits.
If the sum is equal add 1 to the sum, start from the top of the array

## Slide 33
48 in eta
11 in phi
8 x 8 sum
Optical out
1
Optical
Out
2
8x8 sum  optical out
12 of 12 bits sum value
7 bit header, 8 bits BC counter, 1 empty bit
(2x2 sum map)

## Slide 34: Jet trigger
16 optical inputs from EMCAL section
16 optical inputs from HCAL section
Data is organized as 8x8 sum from EMCAL (0.2 eta X0.2 phi)
  Group into 32 (256/8) X 12 (96/8) array.
Data is organized as 2x2 sum from HCAL (0.2 eta X0.2 phi)
  This is done from FEM

## Slide 35
32 in phi
12 in eta
8 x 8 sum maps
when deal with overlapped 4x4 sum (0.8 eta X 0.8 phi) based on the <8X8> sum
done to find jet peak
extend 1st 3 phi columns to larger phi area  convert cylinder to 2D space.

## Slide 36
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | >= | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | >= | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | >= | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | Sm | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | > | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | > | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | >= | >= | >= | > | > | > | > |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 |  |  | 
9 in eta
32 in phi
4x4 overlapped sum ( 0.8 eta and 0.8 phi)
Peak finding algorithm
Search path 3x3

## Slide 37
32 phi
9 in eta
Peaking finding algorithm produces 9X32 map.
valid data array  indicate the peak that pass the threshold
sum value
Encoding routine:
run 9 parallel 32 slides priority encoder
each 32 bits priority encoder is divided into 2 bits encoder
maximum 2 peaks per 32 bits encoder. (5 bits address cover 32 phi)

## Slide 38: Status
The EMCAL portion of LL1 is most complicated
  Cross stitching, peak finding, monitoring etc.
  It is a good shape, couple of weeks of working is required.
The JET physics FPGA code is being revised to match the EMCAL and HCAL hardware, data protocol and format.
Need to write up some documentation

## Slide 39: Backup…

## Slide 40: Digitizer Crate
The Calorimeter digitizer crate system provides
  Interface with GTM through clockmaster Module
    Timing and L0, L1 timing information
  Slow control download and readback
  Mechanical support
  Power entry…

## Slide 41: The Digitizer Subsystem Technical Overview
Controller
clockmaster
GTM
JSEB II
PC
ADC
ADC
XMIT
Trigger
out
Trigger
out
DCM II
crate
(rack based)
Slow control/readback
Beam clock,
L0, L1 trigger
SPHENIX DAQ System
detector
Slow control/readback
bus, L0, L1 trigger
Token passing
dataway
Token passing
dataway
Clock are fanout point to
point through the backplane
Crate based system.
Signals are cable from the on-detector electronics.
Digitized with 14 bit ADC.
Receive timing information the SPHENIX Granule Timing Module (GTM)
Generate L1 trigger primitives
Receive L1 trigger and send out L1 triggered event data to Data Collection Module II (DCMII).
Provide buffer for both the 40 beam crossing L1 delay buffer and 4 L1 triggered events
3 ADC  XMIT
3Gbit/sec
optical link
1.6Gbit/sec
optical link

## Slide 42: Arria 10 FPGA
20nm technology, 10AX570N4NF40I3G
48 transceivers, 6 Gbps upper limit.
570K logic elements  868K registers
1800 20Kbits memory block  35 Mbits
3000 18x19 multipliers.
  Mostly useless for our application…
Core voltage  0.9V, transceiver voltage  0.95V, I/O voltage  1.8V, 2.5V for optical interface.
Transceiver block is separated from core block.
  Easy routing

## Slide 43: Optical ports
Avago/Foxconn/Broadcom 12 port transmitter/receiver
  AFBR-814/AFBR_824 (MiniPot)
Plug in module, size 21.95mmx 18.62mm
Optical wavelength 850nm – up to 150 meter with OM4 4700 Mhz-km fiber.
Up to 10 Gbits/sec
Use 2.5V and 3.3V
Use light turn connector cable  MPO outside
  12 fibers
  Use flat cable
Last order data 3/18/2021
  No replacement alternative…