## Slide 1: Calorimeter Digitizer Electronics
Cheng-Yi Chi
Columbia University

## Slide 2: Off-Detector Calorimeter Digitizer electronics
Function
Past experience
System block diagram
ADC board block diagram, cable test result, differential receivers, ADC choice. Comments on trigger primitives
Progress on the Prototype
Issue/Concern

## Slide 3: Calorimeter Digitizer electronics function
Digitizing the signal after the on-detector electronics with single scale 14 bit ADC.
  Try to maintain the best dynamic range as good we can do with single scale ADC. We are looking for 12 bits dynamic range.
Interface with PHENIX DAQ system
  Receive beam clock, L0 timing and L1 trigger
  Provide the 5 L1 trigger events buffer.
  Provide the functionality to generate L1 trigger primitives.

## Slide 4
Past Experience
FEM Board
Differential
receiver
ADC
(TI’s ADS5272)
ALTERA
FPGA
HBD Pedestal Run
Width s (ch)
Width s (ch)
Mean (ch)
Mean (ch)
Channel #
Channel #
Built
PHENIX Hadron Blind Detector (HBD) off-detector digitizer (12 bits, 60 MHz)
also been use for the MPC readout electronics and Sphenix test beam readout
MicroBoone TPC readout (BNL+Nevis) and PMT readout (similar shaper+ADC like HBD, 64 MHz)
HBD ADC module

## Slide 5
Controller
clockmaster
GTM
JSEB II
PC
ADC
ADC
XMIT
Trigger
out
Trigger
out
DCM II
crate
(rack based)
Slow control/readback
Beam clock,
L0, L1 trigger
PHENIX DAQ System
detector
Slow control/readback
bus, L0, L1 trigger
Token passing
dataway
Token passing
dataway
Clock are fanout point to
point through the backplane
ADC System Block Diagram
Crate based system.
Signals are cable from the on-detector electronics.
Digitized with 14 bit ADC.
Receive timing information the PHENIX Granule Timing Module (GTM)
Generate L1 trigger primitives
(not in the baseline scope)
Receive L1 trigger and send out L1 triggered event data to Data Collection Module II (DCMII).
Provide buffer for both the 40 beam crossing L1 delay buffer and 5 L1 triggered events
4 ADC  XMIT
3Gbit/sec
optical link
1.6Gbit/sec
optical link

## Slide 6
7X ADC clock
F
R
A
M
E
Serialized ADC DATA
De-serializer
Serial
command
L1
Delay
Buffer
5 L1
Accepted
Event
buffer
Token
Passing
Data
ALTERA Arria V GX
BB1D4F35
1152 pins FPGA
Analog
Device
AD9257
8 channel
14bits
65 MHz
ADC
Clock
Fanout
Differential
receiver
6 X beam
clock
2 mm
Hard Metric
or mini-SAS
Connector
Analog
Device
AD9257
8 channel
14 bits
65 MHz
ADC
2 mm
Hard Metric
or min-SAS
Connector
Differential
receiver
Serialized ADC DATA
F
R
A
M
E
7X ADC clock
64 channel
ADC board
6x beam clock
Beam phase,
init, L1
Serialized
Token
Passing
command/
offline data read
De-serializer
Bused command
Serial data
+- 3.5V, -2.5V
Differential
receiver power
+1.8V analog
ADC power
+1.8V digital
ADC power
DC/DC
switch regulator
+4V, -3.5V, +2.5V
Power
+12V
Power
DC/DC
switch regulator
1.5V
LDO
1.1V
core
4V
2.5V FPGA I/O
3.3V
LDO
3.3V
LDO
D
P
U
two transceivers
two transceivers
sPHENIX ADC Module Block Diagram
L1 trigger primitives
transceiver out
RHIC beam clock 9.6MHz

## Slide 7
Analog device AD9249
16 channel 14 bits ADC. Maximum sampling rate 65 MHz SNR 75db
1.8v technology. 58mw per channel at 65 MHz -> 1 W per chip.
144 pins package. 1cm X 1cm BGA
pipeline latency 16 clocks.
Analog Device AD9257
8 channel 14 bits ADC Maximum sampling rate 65 MHz SNR 75.5 db
1.8v technology. 55mw per channel at 65 MHz
65 pins LFCSP package. 0.9mm by 0.9mm.
pipeline latency 16 clocks.
Texas instrument ADS5294
8 channel 14 bits ADC. Maximum sampling rate 80 MHz SNR 75.5db
1.8v technology. Per channel 58mw at 50 MHz, 77mw at 80 MHz.
1-wire only interface only for below 50 MHz sampling
80 pins QFP package. 12mm by 12mm
included digital processing block ( only after digitization)
pipeline latency 11 clocks for 1 wire interface.
Linear Technology LTM9008-14
8 channel 14 bits ADC. Maximum sampling rate 65MHz SNR 73 db
1.8v technology. Per channel 88mw at 65 MHz.
140 pins BGA. 11.25mm X 9mm
pipeline latency 6 clocks.
The limit of ADC LVDS serializer
seems to be less than 1Gbits/sec
65 MHZ ADC
The FPGA does not have 128 LVDS
De-serializer  1 LVDS output
per ADC channel
JSED204B’s ADC need the transceiver to receive data
 Limits number of ADC can be connected to the reasonable price FPGA
The Choice of ADC

## Slide 8
The ADC system is 14 bits (0- 16383 ADC counts)
The ADC input is differential, need to supply both + and – inputs ( peak-peak range is 2V)
(122 mV per ADC counts)
+1V on the positive side and –1V on the negative side
8192 ADC count happened when V+, V- difference is zero
Our signal only swing one side
To get full range we need to offset the signals.  (the point to introduce the noise)

## Slide 9
2mm HM
Input
connector
Differential
receivers
Analog
Device
AD9257
14 bits
ADC
Analog
Power
Trigger
Primitives
output
Serial
Command
output
Serial
Command
input
Clock in
L0/L1
Digital
Power
Token
Passing
Data
In/out
sPHENIX ADC board
64 channel inputs
Mini-SAS / 2mm HM connectors
160mm by 190mm (6U board)
The 8 channel 14 bits ADC will be running at 6x beam crossing rate ~ 60 MHz
Altera Arria 5GX FPGA de-serialize data, provide 5 events buffer, 40 beam crossing L1 delay, token passing data, L1 trigger primitives output
Will do a version of 2mm HM connector  1st choice.
ALTERA
Arria 5GX
FPGA

## Slide 10: Thoughts on the Trigger Primitives.
FEM can do rough gain correction  We will do on board 2x2 sum first
If trigger primitive output will be 8 bits, for 40 Gev top scale, the least count
will be ~156 Mev if the scale is linear.
If we output 8 bits per channels, the optical bandwidth will be
10 ( 8b/10b encoding) *64 * 10 MHz = 6.4 Gbits/sec. if one only output 2X2 sum, we will only have 1.6 Gbits/sec. With formatting, the output will be 2 Gbits/sec. ( 1 frame marker + 1 header + 8* (2* 8) data words.)
if trigger sum is 10 bits, we will have ( 1 frame marker + 1 header + 10 16 bits data words.), The optical
Bandwidth will be 20 (bits)*12 words* 10 MHz = 2.4 Gbits/sec
The FPGA has a high speed transceiver port to the backplane with high speed LVDS repeater. A rear mounted optical transceiver could be used to send out L1 trigger primitives.

## Slide 11: Prototype Progress
ADC Module, Crate Controller and Backplane prototype modules have be build.
  This set is enough for us to test analog function.
    Can we safely built 64 channel ADC module with reasonable performance?
    Will offset circuit introduce more noise into the system?
  The XMIT module is on the way

## Slide 12
Sphenix ADC backplane
Sphenix ADC module
Sphenix crate controller

## Slide 13
ADC Board Performance
(baseline, no signal)
Channel 1 without offset
adc
sigma
Channel number
Channel number
nhits
nhits
nhits
nhits
adc
adc
adc
adc
Ch 0
Ch 1
Ch 2
Ch 3
Baseline
(average ADC)
Baseline
(sigma)

## Slide 14
adc
adc
adc
Baseline
(average ADC)
Channel number
Channel number
Baseline
(sigma)
sigma
Sample number
Sample number
Channel 0
Channel 1
ADC noise test with
old detector HBD preamp

## Slide 15: Cross Talk Study
adc
adc
adc
adc
Sample number
Sample number
Sample number
Sample number
Channel 9
Channel 10
Channel 11
Channel 12
Cross talk with HBD preamp
(similar rise time)

## Slide 16: Production Flow
Last prototype cycle of the electronics should dress production needs.
  Testing, yield etc.
Parts and Printed Circuit Boards (PCB) procurements.
  Work with distributors on getting the parts.
  Work with prototype PCB vendors.
Board assembly.
  Have a preproduction run.
  Work with prototype board assembler.
  Schedule the board delivery to match with testing flow.
    Feedback to assembler.
Testing
  Set up at least 2 test stands.
    One for testing. The other one for debugging.
  Probably can do at least 10 boards a day.

## Slide 17: Cost of the system
The design of the digitizer is trying to minimize the cost of the system.
  Compact 6U design.
    Save space reduce the PCB cost. Saving the rack space. Easy handling.
  Try to use low cost FPGA to all ADC data, event data flow and Level 1trigger primitives.
Except for the clock master module to interface with GTM system, we have design for reset of the system excluding the trigger portion.
  We have ask our vendors for budgetary quotes.

## Slide 18: Status and Outlook
Prototype modules of ADC, Controller and Backplanes has been build.
  Testing ongoing. So far it is O.K.
  XMIT module will be done before end of the year.
Prepare to use the new system for upcoming testing beam
  readout system with 2 ADC modules
Need to test trigger primitives output.
Need to address the test system for the ADC analog inputs.
Some modification is probably necessary for the 2nd round prototype.
  Enhance testing features.

## Slide 19: Backup Slides

## Slide 20
out-
out+
Input +
Input -
Differential Receiver
The ADC module will receive the signal from the
On detector module.
The signal will be AC coupled. The blocking capacitor will be on the frontend.
The ADC’s Vcommon is at 1V. With the signal swing +-0.5v among Vcommon. To get full range
of the ADC, the signal need to swing in both direction. The signal from the detector only swing in one direction.
We offset of the differential receiver to push the baseline to the lower ADC range.
The resistors are discrete components. Supply voltages are adjustable through resistors.
V+
V-
500

## Slide 21
2mm HM cable 10 meters
10 meter Amphenol mini-SAS
extend distance cable
SPHENIX cable
cross talk study
~0.25%
~0.05%

## Slide 22
clock in
Serialized L0,
L1 Data in
USB 3.0 connectors
Optical link from
JSEB II (3 Gbits/sec)
readback
Slow control/
download
Power
Offline
Clock
crystal
Crate Controller
Receive clock and L0 (init, test etc), L1 trigger.
Receive slowdown load from DAQ system.
Write ADC’s module FPGA boot code to the EPROM.
Write ADC, XMIT & Controller modules running parameters.
Download varies table.
Download fake data
Initialize system. Set online/offline system
Provide offline clock/L0 data, L1 trigger.
(standalone crate running)
Provide readback from ADC module to computer.

## Slide 23
Analog Power Section (ADC power, +- differential receiverpower)
Digital Power Section
Slow control/download bus
Readback bus
Token Passing Dataway
Token Passing Dataway
Crate Controller
Point to Point
clock fanout
Crate Backplane

## Slide 24
Digital
Power
Clock in
Token
Passing
Data
In/out
Token
Passing
Data
In/ token out
Serial
Command
input
XMIT Module
Optical transceiver
To DCM II
(1.6 Gbits/sec)
. Receive data from FEM
. Issue token after receive all data transfer
. Format FEM data ( header and checksum)
. Error handling
Altera
Cyclone IV
FPGA