## Slide 1: MBD electronics Design
Measurements
Scope, block diagram etc.
Timing measurement, charge measurement.
Clock Fanout module, backplane & controller.
ADC block diagram, Level 1 trigger discussion.
Test pulse issue
Production

## Slide 2: MBD electronics measurements
The electronics need to measure PMT charge and time and participate local level 1 trigger.
  Measurement window ~25ns
Development cost is high for standalone system.
  We will use calorimeter digitizer system to handle the analog to digital conversion.
  The MBD electronics will do the analog portion of the system, discriminator and charge integrator.
We spilt the PMT pulse into
  1) shaped pulse to be digitizing by 6x BC (~ 60 MHz) 14 bits ADC
  2) converted gated discriminator pulse to shaped pulse and digitized by the same ADC
    Integrated the “ discriminator pulse (rise) and beam gate (falling)” current pulse.
  We are looking at the difference between PMT time.

## Slide 3: Electronics Scope
Small system (128 channels)
  Discriminator+ shaper  Calorimeter digitizer  Local Level 1 trigger
Discriminator system – 128 channels
  8 channel discriminator board
  Backplane + clock fanout board
Calorimeter digitizer system deal with DAQ requirements.
Local Level 1 board is identical to Calorimeter Local level 1 board
  FPGA code change

## Slide 4
GTM
MBD
PMT
Clock
master
Digitizer
Crate controller
shaper
disc
shaper
64 channelCalorim-eter digitizer
Local
Level 1
Trigger
MBD
Clock fanout
~25ns
beam gate
test
pulse
splitter
6x BC clock, mode bits
slow
control
~25ns
beam gate
test
pulse
6x BC
8 channels
MBD Electronics Overview
sPHENIX
timing system
Calorimeter
Clock and Mode Bit
fanout
Beam
Clock

## Slide 5
discriminator
discriminated
Pulse shaper
PMT pulse
shaper
Threshold DAC
MBD Discriminator
Charge
Injector
DAC
Fuse
Zener
diode
Slow
Control
in
Test
pulse
MBD Discriminator Module
Beam Gate input
8 channels of “Discriminator + shaper” < timing> +
“Shaper” <charge>
Passive splitter between timing + charge measurement
Diodes are used to protect input circuits
Comparator is the same one as used in PHENIX beam beam
Electronics.
Shaper is 3 poles shaping, 20ns shaping time
(discrete components)
12 bits DAC to set threshold – one per channel
Charge injector DAC per channel  control through test
Pulse. (EVEN or ODD channels firing)
FPGA are ALTERA MAX series (EPLD)
2mm
HM
connector
2mm
HM
connector

## Slide 6
input
Charge
Injector
Even /odd channel
Firing control
comparator
Standardize
pulse
Pulse width
Beam
Gate
Interface
with shaper
Discriminator Schematic

## Slide 7
Charge gate
Charge injector
signal pulse
Comparators out
Standardized pulse
After gated with
beam window
Test pulse enable
from clock fanout module
Test Pulse  charge injector  Discriminator

## Slide 8
Charge shaper
circuit
Time shaper
circuit

## Slide 9
8 channel 12 bits DAC
Threshold Circuits
Channel by channel
Charge Injector
12 bits DAC
Discriminator DAC

## Slide 10
Chart: 
Chart: 
Chart: 
Chart: 
200ns full scale
2V full scale
Shaping function as function of shaper input
(2ns, 5ns, 10ns, 20ns)
Shaping function is 3 20ns shaper.
Width are define as the discriminator comparator (leading edge) vs beam gate (falling edge)
disc
gate
Shaper input

## Slide 11
MBD clock module
Delay chips
Input from
Calorimeter
Crate controller
Slow
Control
out
TP delay
Test pulse
Beam
Gate
Clock
input
Beam Gate Fanout
TP
out
Receiver clock from Clock Mater module
Generate Beam Gate ( ~25ns)
“AND” operation between clock and /Clock delay
Coaxially fanout all the beam gate pulse to discriminator modules.
Generate 2 test pulse options, test pulse or test pulse + ~1ns (cable delay)
Test pulse delay are set by cables and by 3 set of delay chips (MC100EP196FAG), 80ps per step, 10ns per chip, 30ns range.
Receive slow control from digitizer crate controller
Slow control set
threshold DAC, charge injector DAC
test pulse firing, delay steps,
test pulse option (with or without 1ns delay)
FPGA are ALTERA MAX series (EPLD)
Fine delay
adjustments
MBD Clock Module
Fix delay
jumper
30ns range

## Slide 12
+6, -6V use Molex Z power 76001-0010, 50A capacities. -15 V used for TVC only low current, Use Tyco 9-55556-0 25A each
MBD backplane
Provide Power, slow control
Partial backplane in height. Require modification on the crate side panels. (2 holes).
Estimate power usage -6V ~50A, +6V ~40A, -15V ~ 1A
ERNI 2mm HM power connector 254927 for Power 10.8A current capacity.

## Slide 13
6x clock out
Slow control
readback
Mode Bit
fanout
Slow control
download
Download/readback
Optical connection
JSEB II
6x Clock,
mode bits
Input
MBD command
output
Calorimeter
Crate controller
Through PCIe board, the controller send command to ADC module, XMIT Module and MBD clock fanout modules. It also provide readback path for the ADC modules.
Receive 6x beam clock, mode bits from clock master module.
Fanout 6x beam clock to ADC and XMIT modules

## Slide 14
Test Stand
Discriminator module
Clock fanout module
ADC module
Signal cables
Trigger modules
INPUTS

## Slide 15
7X ADC clock
F
R
A
M
E
Serialized ADC DATA
De-serializer
Serial
command
L1
Delay
Buffer
5 L1
Accepted
Event
buffer
Token
Passing
Data
ALTERA Arria V GX
BB1D4F35
1152 pins FPGA
Analog
Device
AD9257
8 channel
14bits
65 MHz
ADC
Clock
Fanout
Differential
receiver
6 X beam
clock
2 mm
Hard Metric
Analog
Device
AD9257
8 channel
14 bits
65 MHz
ADC
2 mm
Hard Metric
Differential
receiver
Serialized ADC DATA
F
R
A
M
E
7X ADC clock
64 channel
ADC board
6x beam clock
Beam phase,
init, L1
Serialized
Token
Passing
command/
offline data read
De-serializer
Bused command
Serial data
+- 3.5V, -2.5V
Differential
receiver power
+1.8V analog
ADC power
+1.8V digital
ADC power
DC/DC
switch regulator
+4V, -3.5V, +2.5V
Power
+12V
Power
DC/DC
switch regulator
1.5V
LDO
1.1V
core
4V
2.5V FPGA I/O
3.3V
LDO
3.3V
LDO
D
P
U
two transceivers
two transceivers
sPHENIX ADC Module Block Diagram
L1 trigger primitives
transceiver out
RHIC beam clock 9.6MHz

## Slide 16
De-serialize
/alignment
14 bits ADC
serialized data
840 Mbits/sec
LVDS
Input
control
Fake data
512X16
L1 Delay memory
512X128
1-8
Header
512X16
Beam clock
number
6x RHIC
clock
wadd
radd = wadd
- delay
8 events buffer
256 X
1024
1-64 channels
Header
8 x 32
6x RHIC
clock
L1
trigger
BC & L1 event
numbers
Write address
3 bits events,
5 bits samples
read address
3 bits events,
5 bits samples
FIFO
2048 *
34 bits
(first, data,
Last)
write =
valid & token
Read =
!empty
Slow control
readback
Gbits
receiver
Gbits
receiver
16bits
FIFO
16bits
FIFO
Alignment
Gbits
transmitter
80 MHz
Reference
clock
L1 trigger
Primitives
generators
Link control
8b/10b
encoding
Serialized
data
8b/10b
encoding
Serialized
data
from down
Stream board
Token in
Token out
Sphenix
64 channel ADC
Data Flow Diagram
Gbits transmitter
120 MHz
Reference
clock
LVDS repeater
Optical
transceiver
Lemo out
backplane
Daughter card

## Slide 17
Baseline
subtraction
Read address = write address -delay
Delay a parameter
Probably has 2 clocks offset
Dual port memory
Lookup memory
(1024X10)
Read
Address
(upper 10 bits)
Sub = ADC – ADCpre
If (adcpre > adc) sub=0
Load lookup
Memory from
Slow control
10 bits
2X2 SUM
(12 bits output)
only use
upper 8 bits
Choose one of the of of the 12X BC clock phas for trigger primitive
64 channels
16 2X2 8 bits sum
6X BC clock
12X BC Clock
MUX
128 bits
To 8 16 bits
120 MHz clock
10X16 bits FIFO
Transceiver
IP
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
header | Mod + clock | Sum 1+2 | Sum 3+4 | Sum 5+6 | Sum 7+8 | Sum 9+10 | Sum 11+12 | Sum 13+14 | Sum 15+16
delay
+1
+2
+1
+ 1 BC + 2 12X
4 bits trigger phase
Cal trigger primitive Generator (preliminary)
Monitor Delay dual port memory
5 events buffer
L1
trigger
To controller
readout
Delay and
# of Sample
adjustable

## Slide 18
MBD Trigger Primitive data path (preliminary)
ADCs
Post-Pre
Timing
Block
ADCs
Post-Pre
10X10 lookup table
10X10 lookup table
Choose
phase
Choose
phase
Slewing
Correction
12X9
9 bits
3 bits
Time
SUM
Charge
SUM
7 bits
6X beam clock
Time
channels
charge
channels
Trigger
output
2.5 Gbps
8 X16 bits words per beam crossing
optics
ADC clock and discriminator clock are interlock together.. So sample height is fixed for a given PMT pulse time
Beam gate is 25ns  9 bits range will be 50ps per division.
For the timing block we can choose either fix sample relative to BC, peak finder etc…
For 32
channels

## Slide 19
LOCAL LEVE1 Board
36 optical
receivers
12 optical
transmitter
From FEM
To Global
Level 1
. Receive MBD FEM optical data
. Process the data FPGA
. Send Process data to Global Level 1
Altera Arria 10
FPGA

## Slide 20
receiver
Cross stitch
Overlap 2x2 sum
Peak
finder
8x8 sum
receiver
inner/outer HCAL
2X2 sum
EMCAL
HCAL
Pair trigger
JET trigger
receiver
Interaction window / charge
GL 1
MBD
The domain factor of L1 Latency on the optical transmitter/receiver
We have preliminary codes for calorimeter portion of the trigger
The MBD portion of the code is straight forward (hopefully??)
LL1 Block Diagram

## Slide 21: Measurement clocks
Beam Gate is fanout from one module centrally.
  All measurement is relative to this clock.
Digitizer board clock are fanout differentially from crate controller to each module, point to point.
  ADC clock are fanout to individual ADC.
The timing measurements is the difference between channels.

## Slide 22: Possible issue
The test pulse is fanout through the backplane.
  It is mostly designed to be used for initial calibration (single module).
    by walking through delay chips steps and fix delay insertion.
  We don’t know exactly the effect of the test pulse propagation on fully loaded backplane.
    the added jitters and time shift.
    The final calibrations will be done through the beam data.

## Slide 23
PECL->
LVDS driver
LVDS receiver
LVDS -> CMOS
8 channel fanout
(clock)
100 ohms
termination
100 ohms
termination
8 channel charge injectors
Test pulse
generator
Clock
module
Discriminator
module
LVDS receiver
LVDS -> CMOS
8 channel fanout
(clock)
8 channel charge injectors
Discriminator
module
LVDS receiver
LVDS -> CMOS
8 channel fanout
(clock)
8 channel charge injectors
Discriminator
module
LVDS receiver
LVDS -> CMOS
8 channel fanout
(clock)
8 channel charge injectors
Discriminator
module
16 discriminator modules in the system, 8 modules per sides
0.8 inch space between modules
The discriminator modules will act like stubs
4mm trace length between LVDS receiver and backplane connector
Discriminator Test Pulse
Propagation

## Slide 24: What need to be done for production
On the prototype system
  We built 3 backplanes, 3 discriminator modules and 3 clock fanout modules
For discriminator board
  We need to swap the power ground pins on one of the chip
  Add more ground connection on the power connectors
  These two changes are done on the prototype module
  Add additional bypass capacitor per comparator.
    Did not seen much effect on the prototype modules but recommended by manufacture.
We will test all the discriminator modules in Nevis.

## Slide 25: Backup slides

## Slide 26
Beam
window

## Slide 27
Test Pulse
Test pulse enable
from slow control